## Slide 1
EE-371 : Control Systems
Lecture#02
Introduction to Control Systems
Chapter #01
Text Book: Control Systems Engineering by Norman S. Nise 5th Edition
Instructor: Ms Neelma Naz
Class: BEE 12 C/D
School of Electrical Engineering and Computer Science
Department of Electrical Engineering

## Slide 2: Types of Control System
A system designed to follow a changing reference is called tracking control or servo.
A system designed to maintain an output fixed regardless of the disturbance present is called a regulating control or a regulator.

## Slide 3: Parts of Control System
In their simplest form, control systems take in data as input, process the data, and then send out signals as output…

## Slide 4: Types of Control System
There are two main types of control system…
Open Loop
System
Closed Loop
System
&

## Slide 5
A person steps on a pressure pad, and the pressure pad sends a signal to the control box
The control box processes the data, and sends a signal to the electric door
The door opens in time for the person to walk through
Open Loop System
The open loop system is the simplest type of control system, as it does not take account of the output. The input data is processed, then sent as output, e.g. an automatic door…

## Slide 6
NUST
(Plant)
Students
(Actuator)
Teaching
Activities
(Controller)
NUST
Environment
Disturbance
Parties, Chit Chat
Games, TV, Net
Output
Result
For students in a College, a …???…..loop College environment is shown in a block diagram (system with NO REGULAR check (Feedback) on the students). If there are no quizzes, home assignments, midterm exams, we call that system as an …………………………… (Open Loop / Closed Loop ??)
Yearly
Exam
Performance
Students
Intake
Example of Open-Loop System i.e without Feedback
6

## Slide 7: Feedback
Feedback is a key tool that can be used to modify the behavior of a system.
This behavior altering effect of feedback is a key mechanism that control engineers exploit deliberately to achieve the objective of acting on a system to ensure that the desired performance specifications are achieved.
Notes: Feedback is a very heart of control. Three examples are given for feedback systems in the book. Students are encouraged to read Section 1.2.

## Slide 8
Closed Loop System
A closed loop system uses feedback provided by sensors. Feedback is where information from the output gets used as part of the input. A feedback loop provides extra data, which is processed with the input data.

## Slide 9
Most control systems are closed loop systems. For example
Closed Loop System
Controller
NUST
(Plant)
Students
(Actuator)
Teaching
Activities
(Controller)
NUST
Environment
Reference
(Standard)
(Sensor)
End & Mid,Terms
Quizes, Labs
Assignments
Output
Result
+
-
Error
Disturbance
Parties, Chit Chat
Games, TV, Net
Notes: For students in a College, a …???…… loop College environment is shown in a block diagram (system with regular check on the students). If there are no quizzes, home assignments, midterm exams, we call that system as
an …………………………….(Open/Closed loop)

## Slide 10: Flight Control System
The pilot operates the control to put the aircraft into a steep turn.
Feedback also forms part of the input.
The plane’s control box (a large computer) processes this data and sends signals to the wing flaps and engines.
The wing flaps and engines make the necessary adjustments.
Sensors monitor the tilt of the aircraft and send this information to the control box. This becomes part of the input. When the required amount of tilt has been reached, the computer sends signals to the wing flaps and engine to stop any further adjustments.

## Slide 11: Human Body Example
Output Position
Desired
position
R (s)
Hand
G(s)
Disturbance Forces
U (s)
Y(s)
Neural Signal
Reference
Input
Control algorithm (Brain)
Controller
Plant
Muscle
Actuator
Eye
Sensor
Open loop
Closed loop
Control block
No Feedback
With Feedback
11

## Slide 12: Multivariable Control System
Desired Output Response
Measurement
Output Variables
Controller
Process
Multi Input Multi Output (MIMO) System

## Slide 13: Classification of Control Systems
Control Systems
Natural
Man-made
Manual
Automatic
Open-loop
Closed-loop
Non-linear
linear
Time variant
Time invariant
Non-linear
linear
Time variant
Time invariant
LTI Control Systems(Linear time invariant control systems)
13

## Slide 14: What is the Control System Engineer trying to achieve? (Analysis and Design Objectives)
First, understand the broader picture of the
application to best apply a suitable control system.
A good control system is a system that will
  generate a response quickly and without oscillation (good transient response),
  have low error once settled (good steady-state response),
  and will not oscillate wildly or damage that system (stability).

## Slide 15
Consider an elevator. When the fourth-floor button is pressed, the elevator rises to the fourth floor with a speed and floor-leveling accuracy designed for passenger comfort.
Control Systems (Example)
Two measures of performance are :
(1) the transient response
(2) the steady-state error.
Passenger comfort and passenger patience are dependent upon the transient response
15

## Slide 16
Antenna azimuth position control system:
system concept
detailed layout
16

## Slide 17
Antenna azimuth position control system:
Schematic diagram
functional block diagram
17

## Slide 18
Response of a position control system showing effect of high and low controller gain on the output response

## Slide 19: Control System Classification
Open-Loop Control System
Missile Launcher System

## Slide 20: Control System Classification
Closed-Loop Feedback Control System
Missile Launcher System

## Slide 21
The control system design process
21

## Slide 22
Electro-Mechanical
Actuator is a device which converts energy from one form to another. e.g: microphone, thermometer, loud speaker, antenna and many more.
Energy
Electrical
Thermal
Fluid
Hydraulic
Pneumatic
Mechanical
Chemical
Actuator
Motion
Rotary
Linear
Complex
What is a Actuator?

## Slide 23
What is a sensor?
Measurement
Temperature
Force
Distance
Speed
Sensor
Electrical Signals
Voltage
Sensors are transducers that produce (transform) electrical energy (signals) as a result of some type of stimulation (measurement space)
Voltage
Current
Digital