## Slide 1: Discrete-Time Filter Design by Windowing Chapter-7
Content and Figures are from Discrete-Time Signal Processing, 2e by Oppenheim, Shafer, and Buck, ©1999-2000 Prentice Hall Inc.

## Slide 2: Filter Design by Windowing
Simplest way of designing FIR filters
Method is all discrete-time no continuous-time involved
Start with ideal frequency response
Choose ideal frequency response as desired response
Most ideal impulse responses are of infinite length
The easiest way to obtain a causal FIR filter from ideal is
More generally

## Slide 3: Windowing in Frequency Domain
Windowed frequency response
The windowed version is smeared version of desired response
If w[n]=1 for all n, then W(ej) is impulse train with 2 period (practically speaking)

## Slide 4: Properties of Windows
Prefer windows that concentrate around DC in frequency
  Less smearing, closer approximation
Prefer window that has minimal span in time
  computationally efficient
So we want concentration in time and in frequency
  Contradictory requirements
Example: Rectangular window

## Slide 5: Properties of Windows

## Slide 6: Rectangular Window
Narrowest main lob
  4/(M+1)
  Sharpest transitions at discontinuities in frequency
Large side lobs
  -13 dB
Simplest window possible

## Slide 7: Bartlett (Triangular) Window
Medium main lob
  8/M
Side lobs
  -25 dB
Simple equation

## Slide 8: Hanning Window
Medium main lob
  8/M
Side lobs
  -31 dB
Equation

## Slide 9: Hamming Window
Medium main lob
  8/M
Good side lobs
  -41 dB
Equation

## Slide 10: Blackman Window
Large main lob
  12/M
Very good side lobs
  -57 dB
Complex equation

## Slide 11: Incorporation of Generalized Linear Phase
Windows are designed with linear phase in mind
  Symmetric around M/2
So their Fourier transform are of the form

## Slide 12: Linear-Phase Lowpass filter
Desired frequency response
Corresponding impulse response
Desired response is even symmetric, use symmetric window

## Slide 13: Kaiser Window Filter Design Method
Parameterized equation forming a set of windows
  Parameter to change main-lob width and side-lob area trade-off
  I0(.) represents zeroth-order modified Bessel function of 1st kind

## Slide 14: Determining Kaiser Window Parameters
Given filter specifications Kaiser developed empirical equations
  Given the peak approximation error  or in dB as A=-20log10 
  and transition band width
The shape parameter  should be
The filter order M is determined approximately by

## Slide 15: Example: Kaiser Window Design of a Lowpass Filter
Specifications
Window design methods assume
Determine cut-off frequency
  Due to the symmetry we can choose it to be
Compute
And Kaiser window parameters
Then the impulse response is given as

## Slide 16: General Frequency Selective Filters
A general multiband impulse response can be written as
Window methods can be applied to multiband filters
Example multiband frequency response
  Special cases of
    Bandpass
    Highpass
    Bandstop