## Slide 1: EE-357: CCN Introduction to Physical Layer
Hassaan Khaliq Qureshi
School of Electrical Engineering & Computer Science
National University of Sciences & Technology (NUST)
Pakistan.

## Slide 2: Typical Communication System
Transmitter
Information source
Channel
Receiver
Information sink

## Slide 3: The Components
Transmitter
Receiver
Medium
  Carries electromagnetic waves. Can be :
    Guided medium
      e.g. twisted pair, optical fiber
      In this course, the focus is on the
    Unguided medium
      wireless
        e.g. air, water

## Slide 4: Bandwidth and Data Rate

## Slide 5: Radio Waves
Image courtesy of Prof. Andrea Goldsmith’s lecture notes
Notes: Ionizing (or ionising) radiation is radiation composed of particles that individually carry enough kinetic energy to liberate an electron from an atom or molecule, ionizing it.
Ionizing radiation is generated by very high temperature or due to acceleration of charged particles by the electromagnetic fields produced by natural processes. The Ultraviolet to Gamma range is Ionizing.

## Slide 6: Radio Waves
Radio waves are characterized by:
  Oscillating in time at a frequency, f
  Travelling through the air at speed of light, c
  Distance covered by one cycle of the wave or wavelength, λ
Wavelength and Frequency are inversely proportional
Notes: As the frequency is increased the amount of interference caused by the atmosphere reduces...as higher frequency signal has more signal energy in it....so it can penetrate the atmosphere more easily...(the same reason why we use modulation with higher frequency)

## Slide 7: Sine Wave – Defining Characteristics
A sine wave is a fundamental periodic signal
Can be represented by three parameters
Peak Amplitude (A)
  maximum strength of signal
  volts
Frequency (f)
  Rate of change of signal
  Hertz (Hz) or cycles per second, or times it repeats per second
    Mains electricity is 60Hz
  Period = time for one repetition (T)
    T = 1/f (an inverse relationship)
Phase ()
    Relative position in time with a single period of the signal
    Consider it like this:
      Move the Y axis and indicate if its to the left (leading) or right (lagging)
Notes: the phase, specifies where in its cycle the oscillation begins at t = 0.

## Slide 8: Sine Wave – Defining Characteristics
A sine wave is a fundamental periodic signal
Can be represented mathematically as
  s(t) = A sin (t + )
    A is amplitude,  is the angular velocity and  is the phase
     is measured in radians per sec.
    Engineers tend to prefer to describe this using ‘f’ for frequency, measure in Hz
  s(t) = A sin (2ft + )
Notes: An arc of a circle with the same length as the radius of that circle corresponds to an angle of 1 radian. A full circle corresponds to an angle of 2π radians.
Last class question: WiMAX (Worldwide Interoperability for Microwave Access)

## Slide 9: Signal Bandwidth versus Channel Bandwidth
A signal is usually made up of sinusoidal signals of varying frequencies
  It can be shown (Fourier analysis) that any signal is made up of component sine waves
  A given function or signal can be converted between the time and frequency domains with a pair of mathematical operators called a transform.
  An example is the Fourier transform, which decomposes a function into the sum of a (potentially infinite) number of sine wave frequency components. The 'spectrum' of frequency components is the frequency domain representation of the signal.
Notes: A frequency-domain representation can also include information on the phase shift that must be applied to each sinusoid in order to be able to recombine the frequency components to recover the original time signal.
The inverse Fourier transform converts the frequency domain function back to a time function.

## Slide 10: Frequency Domain Concept
Why we analyze the signal in the frequency domain?
A frequency-domain graph shows how much of the signal lies within each given frequency band over a range of frequencies.
A given function or signal can be converted between the time and frequency domains with a pair of mathematical operators called a transform.
Hence, we can have an equivalent representation of any signal in the frequency domain
Notes: Fourier transform for frequency domain and Inverse for time domain.

## Slide 11: Signal Bandwidth versus Channel Bandwidth
(4/)*( sin(2(1f)t) +(1/3)sin (2 (3f)t) )
Image courtesy of William Stallings’ lecture notes

## Slide 12: Signal Bandwidth versus Channel Bandwidth
Can you see how we can represent the following signal in terms of its sinusoidal components?
Image courtesy of William Stallings’ lecture notes
(4/)*( sin(2(1f)t) +(1/3)sin (2 (3f)t) )
Notes: So Here we see a frequency domain function S(f) that specifies the peak amplitude of the constituent frequencies of the signal s(t)=
(4/)*( sin(2(1f)t) +(1/3)sin (2 (3f)t) )
This means we have a component at f of magnitude 4/ = 1.27 and another at 3f of magnitude 4/*1/3 = 0.42
Its bandwidth is 3f – 1f = 2f

## Slide 13: Signal Bandwidth versus Channel Bandwidth
Difference between maximum and minimum frequency components of a signal is generally referred to as:
  Signal bandwidth, information bandwidth, source bandwidth, absolute bandwidth …
  Some signals have infinite bandwidth, but still have a narrow effective bandwidth
    Narrow band of frequencies containing most of the energy
The bandwidth available on the channel is referred to as:
  Channel bandwidth, medium bandwidth, transmission bandwidth, available bandwidth…
Notes: An infinite-bandwidth white noise signal is a purely theoretical construction

## Slide 14: Signal Bandwidth versus Channel Bandwidth
Spectrum
  range of frequencies contained in the signal
    Here it extends from f to 3f
Absolute bandwidth
  width of spectrum
    Here its 2f
Effective bandwidth
  Often just bandwidth
  Narrow band of frequencies containing most of the energy
DC Component
  Component of zero frequency
Effective bandwidth
Notes: When describing a periodic function in the frequency domain, the DC bias, DC component, DC offset, or DC coefficient is the mean value of the waveform. If the mean amplitude is zero, there is no DC offset

## Slide 15: Exercise
Lets have an approximation of a square wave with more and more components
  a) (4/)*( sin(2(1f)t) +(1/3)sin (2 (3f)t) )
  b) (4/)*( sin(2(1f)t) +(1/3)sin (2 (3f)t) +(1/5)sin (2 (5f)t) )
  c) (4/)*( sin(2(1f)t) +(1/3)sin (2 (3f)t) +(1/5)sin (2 (5f)t) +(1/7)sin (2 (9f)t) )
  a) If we had a signal frequency of 106Hz(1Mhz) these would have bandwidths of
  b) If we had a signal frequency of 2*106Hz(2Mhz) these would have bandwidths of

## Slide 16: Answer to the Exercise
  If we had a signal frequency of 106Hz(1Mhz) these would have bandwidths of
  a) Extreme components at 1f and 3f = Bandwidth of 2f = 2 *106 = 2 MHz
  b) Extreme components at 1f and 5f = Bandwidth of 4f = 4 *106 = 4MHz
  c) 8MHz
  If we had a signal frequency of 2*106Hz(2Mhz) these would have bandwidths of
  a) Extreme components at 1f and 3f = Bandwidth of 2f = 2 *2*106 = 4 MHz
  b) Extreme components at 1f and 5f = Bandwidth of 4f = 4 *2*106 = 8MHz
  c) 16MHz

## Slide 17: Signal Bandwidth versus Channel Bandwidth
Signal bandwidth should be lesser than the medium bandwidth for the signal to be transmitted accurately
If the signal bandwidth is greater than the medium bandwidth, then some of the signal’s frequency components are truncated during transmission
Generally, the signal is passed through a band limiting filter before modulation

## Slide 18: Signal Bandwidth versus Channel Bandwidth
Can you see how we can represent a square wave in terms of its sinusoidal components?

## Slide 19: Signal Bandwidth versus Channel Bandwidth
Can you see how we can represent a square wave in terms of its sinusoidal components?
Image courtesy of William Stallings’ lecture notes

## Slide 20: Signal Bandwidth versus Channel Bandwidth
As we add more frequency components, the signal becomes more and more exact
But the signal frequency increases and it might not fit in the channel bandwidth
Thus an inherent tradeoff between signal and channel bandwidths exists
Image courtesy of William Stallings’ lecture notes

## Slide 21: Signal Bandwidth versus Channel Bandwidth
For a ‘real world’ square wave the more frequency components it has, the better it approximates the ideal signal
You probably want your real signal to be as close as possible to the ideal.

## Slide 22: Exercise
Can you draw the frequency domain representation of:
  (4/)*( sin(2ft) +(1/3)sin (2 (3f)t) +(1/5)sin (2 (5f)t) +(1/7)sin (2 (7f)t) )
  Steps
    Identify all the components
    Determine the magnitude of each
    Draw graph
Show that its bandwidth is 6f.
Notes: If a signal has a DC component then it will shift bit further to the level of the DC component.

## Slide 23: Bandwidth and Data Rate
Consider a transmitter uses the following approximate sine wave to send binary (0,1) symbols
What is the bandwidth of one cycle of this signal?
Image courtesy of William Stallings’ lecture notes

## Slide 24: Bandwidth and Data Rate
Consider a transmitter uses the following approximate sine wave to send binary (0,1) symbols
What is the bandwidth of one cycle of this signal?
5-1 = 4 Hz
Image courtesy of William Stallings’ lecture notes

## Slide 25: Bandwidth and Data Rate
Signal Bandwidth of one cycle: 5-1 = 4 Hz
If the channel bandwidth is 4MHz, how many cycles of this signal can we transmit in the available bandwidth?
Image courtesy of William Stallings’ lecture notes

## Slide 26: Bandwidth and Data Rate
Signal Bandwidth of one cycle: 5-1 = 4 Hz
If the channel bandwidth is 4MHz, how many cycles of this signal (mentioned above) can we transmit?
4 Hz for one cycle
1 million cycles in 4 MHz
Image courtesy of William Stallings’ lecture notes
Notes: There is a direct relationship between data rate and bandwidth: the higher the data rate of a signal, the greater is its required effective bandwidth.
Although a given waveform may contain frequencies over a very broad range, as a practical matter any transmission system (transmitter plus medium plus receiver) will be able to accommodate only a limited band of frequencies. This, in turn, limits the data rate that can be carried on the transmission medium.
What is the data rate (bits/sec) that we can achieve?
106 cycles ----------- 1 sec
1 cycle ------------- 1µ sec
2 bits ------------- 1µ sec
1 bit -------------- 0.5µ sec
=> Data rate = 2 Mbps can be achieved?

## Slide 27: Data Rate and Bandwidth
Any transmission system has a limited band of frequencies which limits the data rate that can be carried
However, the limited bandwidth increases distortion
Therefore, a direct relationship between data rate & bandwidth exists.

## Slide 28: Bandwidth and Data Rate
There is a direct relationship between data rate and bandwidth [see next slide]: the higher the data rate of a signal, the greater is its required effective bandwidth and so the channel bandwidth or medium bandwidth
Although a given waveform may contain frequencies over a very broad range, as a practical matter any transmission system (transmitter plus medium plus receiver) will be able to accommodate only a limited band of frequencies.
This, in turn, limits the data rate that can be carried on the transmission medium.

## Slide 29: Shannon Equation
The larger the bandwidth the higher the transmission speed
The stronger the signal, the higher the transmission speed
The ‘louder” the noise, the lower the transmission speed
Shannon Equation:
Maximum Data rate = Bandwidth * Log2 (1 + Signal Power/Noise)
Claude Shannon, A Mathematical Theory of Communication, 1948

## Slide 30: Bandwidth and Throughput
Bandwidth and throughput are two of the most confusing terms used in networking; primarily, because it can be defined in various ways.
Bandwidth is literally the width of frequency band; e.g., voice-grade telephone can support frequencies from 300 Hz to 3300 Hz and said to have a bandwidth of 3KHz.

## Slide 31: Bandwidth and Throughput
When we talk to bandwidth of a link, we usually refer to the number of bits per second that can be transmitted on the link. We might say that the bandwidth of an Ethernet link is 10 Mbps.
More generally, we tend to use the term throughput to refer to the measured performance of the system. E.g., due to various inefficiencies, a pair of nodes connected by a link of 10 Mbps may achieve a throughput of only 2 Mbps.

## Slide 32
Throughput and bandwidth
The theoretical number of bits that can be sent per second = bandwidth
The measured number of bits that can be successfully sent per second = throughput
Instantaneous and average throughput

## Slide 33: The Politics of the Electromagnetic Spectrum
ISM and U-NII bands used in the United States by wireless devices
Notes: White Spaces: Frequency bands that have been allocated but are not being used locally.
Unlicensed National information infrastructure

## Slide 34: The Politics of the Electromagnetic Spectrum
Notes: White Spaces: Frequency bands that have been allocated but are not being used locally.
Unlicensed National information infrastructure